## Slide 1: OpenDRIVE XODR Maps in MATLAB
Prof. Craig Beal
Bucknell University
Started: 3.25.22
Updated through: 5.13.22

## Slide 2: OpenDRIVE XODR file basics
As applicable for import into MATLAB for plotting/analysis

## Slide 3: OpenDRIVE XODR
Roads are defined in a hierarchical XML format
  OpenDRIVE
    Header  bounding box defined by west, east, south, north limit values
    Roads (multiple)
      Planview
        Geometry (multiple)
          Line  start point in E,N coords, start point in s coord, heading, length
          Arc  start point in E,N coords, start point in s coord, initial heading, length, curvature
          Spiral  start point in E,N coords, start point in s coord, initial heading, length, initial curvature, ending curvature
          Parametric polynomial
      Lanes
        Lane Segment(multiple) -> start point in s coord
          Left, Center, Right
            Lane (multiple)
              Width (multiple)-> cubic polynomial form defining profile in s,t coordinates
              RoadMark ->
      Objects
        Object (multiple)
          Location of object origin in S,T coords
          Bounding box (length, width or radius of circle in u,v coords)
          Outline
            Corners in S,T coords or local u,v coords
          Repeat element to repeat objects with linearly varying parameters
OpenDRIVE 2.0 will break almost everything that depends on these definitions!!!

## Slide 4: OpenDRIVE -> MATLAB
Importing OpenDRIVE data to MATLAB is fairly straightforward
  There exist several xml2struct tools that can convert the XML into a MATLAB structure that preserves the hierarchy of the OpenDRIVE road structure.
  Interpretation of the XML is so-so:
    Fields are properly labeled according to the associated XML element
    Multiple fields (e.g. roads, geometry elements of a road, objects) are listed in structure arrays, which make sense
    All data values at the lowest level of the “tree” are represented in strings and must be converted with str2num() or str2double() for calculations in MATLAB
    Every element has a separate “Attributes” structure rather than including the attributes in the element itself, leading to “deeper” addressing of the actual data

## Slide 5: Good parts of OpenDRIVE structure in MATLAB
Cell arrays are used anywhere multiple elements exist at a level
  Easy to iterate over the cell arrays (though requires loops)
Easy to compute (X,Y) coords from (S,T) representation
Each segment has initial pose (x0,y0), h0 and s0 plus the geometry descriptors and can thus be loaded/plotted separately from the others
Objects can be “indexed” by station to determine which segment to compute the geometry from
  The initial pose of the segment allows for “local” computations using the segment initial values rather than referencing the road start

## Slide 6: Bad parts of OpenDRIVE structure in MATLAB
The xml2struct function produces inconsistent structure hierarchies when layers contain only a single element
  Cell arrays of structures for multiples, structure for singles
  Addressed by fcn_RoadSeg_convertXODRtoMATLABStruct()
Reliant on proper XODR formatting to ensure segment ordering is correct (in order of increasing station)
  Addressed by fcn_RoadSeg_XODRSegmentChecks()
Malformed segments or inconsistencies in XODR will transfer through to the MATLAB structure
  May need to have a MATLAB routine to check that (xF,yF) as well as hF at sF matches with (x0,y0) as well as h0 at s0 of the next segment
  Addressed by fcn_RoadSeg_XODRSegmentChecks()
Need a separate lookup table to correlate objects with the road geometry segment they are located with respect to
Lanes are defined section-by-section and can “shift” identifier from one section to the next if a lane appears (begins with zero width and widens) or disappears (narrows to zero width) at the lane section boundary
Objects do not have any built-in attributes for appearance (e.g. color)
  Can be stored in <userData> within the object elements

## Slide 7: MATLAB Tools for OpenDRIVE Parsing/Plotting

## Slide 8: fcn_RoadSeg_convertXODRtoMATLABStruct()
Input: OpenDRIVE *.xodr file
Output: MATLAB structure, with nested hierarchical elements consistent with the OpenDRIVE specification

## Slide 9: Key Functionalities for MATLAB -> XODR
Construction of XODR files
  Scripted construction given a particular MATLAB struct
  Interactive construction of XODR file
  Dependencies:
    Create road segment from given start station and parameters
    Calculate (e,n,h) from segment and start
Conversion of recorded data to XODR files
  Fitting of XODR parameterized segments from data
  Conversion of XODR segments into XODR MATLAB structure
  Check for proper XODR construction (consistency checks)
  Writing to XODR file

## Slide 10: Key Functionalities for XODR -> MATLAB
Parsing road centerlines from XODR files
Parsing lane boundaries from XODR files
Parsing objects from XODR files
  How to represent signs?
  UserData field option for storing “other” info
    Color, smart/no, sign message
Plotting road/lane geometries and objects from XODR files

## Slide 11: Key Functionalities
Interactive construction of XODR files
  Status: geometry works, missing road/lane linkage and objects
Conversion of recorded data to XODR files
  Status: not started, most of the tools needed in the chain exist
Parsing road centerlines from XODR files
  Status: complete
Parsing lane boundaries from XODR files
  Status: complete, may need upgrades for better handling of lane bounds
Parsing objects from XODR files
  Status: complete
Plotting road/lane geometries and objects from XODR files
  Status: mostly complete, does not handle junctions or non-driving lanes well

## Slide 12: Construction of XODR files

## Slide 13: Filling the header

## Slide 14: Describing the path (line)

## Slide 15: Describing the path (arc)

## Slide 16: Describing the path (spiral)

## Slide 17: Setting lane offsets

## Slide 18: Setting lane sections

## Slide 19: Lane Linkage
Need to determine which lanes “appear” or “vanish” as
the sections progress in order of increasing station. In the
example below, two right lanes in the first lane section become three right lanes in the second. The first lane
(closest to the center) continues, as does the third lane (the shoulder), so lane 2 in the second section is the “appearing” lane. This means is has no predecessor.
Similarly, lanes can disappear, in which case they simply
have no lane that refers to it as a predecessor. The MATLAB
code does not use successor elements, but they can be included for completeness. A table of the links for the example is provided below. These are entered into the
structure or XODR file manually.
None | None | None | None | None | None
-3 | None | -1 | 0 | 1 | 2
-3 | -2 | -1 | 0 | 1 | 2