## Slide 1: OpenDRIVE XODR Maps -> MATLAB
Prof. Craig Beal
Bucknell University
3.25.22

## Slide 2: OpenDRIVE XODR
Roads are defined in a hierarchical XML format
  OpenDRIVE
    Header  bounding box defined by west, east, south, north limit values
    Roads (multiple)
      Planview
        Geometry (multiple)
          Line  start point in E,N coords, start point in s coord, heading, length
          Arc  start point in E,N coords, start point in s coord, initial heading, length, curvature
          Spiral  start point in E,N coords, start point in s coord, initial heading, length, initial curvature, ending curvature
          Parametric polynomial
      Objects
        Object (multiple)
          Location of object origin in S,T coords
          Bounding box (length, width or radius of circle in u,v coords)
          Outline
            Corners in S,T coords or local u,v coords
          Repeat element to repeat objects with linearly varying parameters
OpenDRIVE 2.0 will break almost everything that depends on these definitions!!!

## Slide 3: OpenDRIVE -> MATLAB
Importing OpenDRIVE data to MATLAB is fairly straightforward
  There exist several xml2struct tools that can convert the XML into a MATLAB structure that preserves the hierarchy of the OpenDRIVE road structure.
  Interpretation of the XML is so-so:
    Fields are properly labeled according to the associated XML element
    Multiple fields (e.g. roads, geometry elements of a road, objects) are listed in structure arrays, which make sense
    All data values at the lowest level of the “tree” are represented in strings and must be converted with str2num() or str2double() for calculations in MATLAB
    Every element has a separate “Attributes” structure rather than including the attributes in the element itself, leading to “deeper” addressing of the actual data

## Slide 4: Good parts of OpenDRIVE structure in MATLAB
Cell arrays are used anywhere multiple elements exist at a level
  Easy to iterate over the cell arrays (though requires loops)
Easy to compute (X,Y) coords from (S,T) representation
Each segment has initial pose (x0,y0), h0 and s0 plus the geometry descriptors and can thus be loaded/plotted separately from the others
Objects can be “indexed” by station to determine which segment to compute the geometry from
  The initial pose of the segment allows for “local” computations using the segment initial values rather than referencing the road start

## Slide 5: Bad parts of OpenDRIVE structure in MATLAB
The xml2struct function produces inconsistent structure hierarchies when layers contain only a single element
  Cell arrays of structures for multiples, structure for singles
  Addressed by fcn_RoadSeg_convertXODRtoMATLABStruct()
Reliant on proper XODR formatting to ensure segment ordering is correct (in order of increasing station)
  Addressed by fcn_RoadSeg_XODRSegmentChecks()
Malformed segments or inconsistencies in XODR will transfer through to the MATLAB structure
  May need to have a MATLAB routine to check that (xF,yF) as well as hF at sF matches with (x0,y0) as well as h0 at s0 of the next segment
  Addressed by fcn_RoadSeg_XODRSegmentChecks()
Need a separate lookup table to correlate objects with road geometry segments
Objects do not have any built-in attributes for appearance (e.g. color)
  Can be stored in <userData> within the object elements

## Slide 6: Needed code
OpenDRIVE to MATLAB work zone scenario
  OpenDRIVE to road reference line
    Extract X,Y points, generate path, convert to traversal
    Plot using the traversal plotting functions in the path library
  OpenDRIVE to lane boundaries
    Extract X,Y points, generate path, convert to traversal
    Plot using the traversal plotting functions in the path library
  OpenDRIVE to world objects
    If cornerroad or cornerlocal provided, extract X,Y points, convert to patch object
    If only radius provided, create circular patch object at given location
    If only heading, length, width provided, create rectangular patch object at given location
    Plot patch objects using the patch plot functions in the patch library