## Slide 1: What changes in the code
Phakphum artkaew

## Slide 2
- Specify the format of numbers as %e which will express number as exponent and decimal places

## Slide 3
The version of revMinor needs to be changed to 4 because RR 2020 supports up to 4
Added the program element which the value is RoadRunner
Added the version element which the value is R2022a Update 1 (1.4.1.c40ee10fc8)
Added the name element

## Slide 4
Added user input asking for the type of road, speed limit, and unit limit because we need these tags in xodr file

## Slide 5
Added s attributes in the road tag. Using the value 0 according to RR xodr
Added typeRoad element
Added speedLimit element
Added unitLimit element
Removed the s elements from the road tag
Changed road id to 0
Use the name Road 0 for the road name
Added junction elements and put value of -1

## Slide 6
Added elevationProfile tag
Added lateralProfile tag

## Slide 7
Added user input singleSide. The program will ask user for singleSide and the user will type false or true
Then we put that value into singleSide element in laneSection tag

## Slide 8
Modified the lane info to ask more information from user. The information includes a,b,c,d,type,level,color,laneChange
and travelDir
The same goes for the right lane but the difference is left lane will go from shoulder to driving and right lane will go from
driving to shoulder

## Slide 9
Added more tags: level, roadMark, speed, and userData
If else statement for separating driving and other. Driving lane has solid type and with is difference

## Slide 10
The Center lane is unique
Type needs to be solid solid
Color needs to be yellow
Width needs to be 0.125